## Slide 1: Computer Architecture
The mainboard

## Slide 2: Lecture Objectives
Introduction to the Arduino Uno and development equipment
Preparation for the lab activities

## Slide 3
CPU
RAM
ROM
I/O
Address BUS
Data BUS
Control BUS

## Slide 4: Development Equipment
Mainboard
  Arduino Uno & PC USB cable
Integrated Development Environment
  Allows you to write and upload programs
  Note that this is only available in W201
Breadboard
  Allows components to be wired to the Arduino

## Slide 5
The Mainboard:
Arduino Uno

## Slide 6
Arduino Uno I/O
We won’t be using analog pins
to PC

## Slide 7: Atmel ATMega328 Processor
CPU – 8-bit Atmel AVR (16MHz)
FLASH – 32kBytes
RAM – 2kBytes
EEPROM – 1kBytes
Input Output
  Analog/Digital
  PWM
  Comms - Serial, I2C, SPI

## Slide 8: Development Platform
Arduino has no operating system.
Initialises it’s hardware via it’s BIOS.
No direct user interaction.
Requires a development platform.
The development platform exists on a PC.

## Slide 9: Integrated Development Environment
We need a PC based IDE to interact with Arduino
This allows us to:
  Write the software
  Compile it into a binary image
  Upload this to the Arduino
This is programmed into FLASH memory
  Once done, it can operate independently

## Slide 10: Breadboards
To wire components together easily
Consist of pin sockets hardwired in rows

## Slide 11: Breadboards
To wire components together easily
Consist of pin sockets hardwired in rows

## Slide 12
Traffic Lights

## Slide 13: Breadboards – Traffic Lights

## Slide 14: Arduino IDE
Connect to PC using USB cable
Launch the IDE:
  Path:
    All programs
    Computing
    Arduino
    arduino

## Slide 15: 1. Configure IDE
Select Board
Select Serial Port
Comport will be SECOND port in list
If only 1 appears:
  close down IDE
  plug in Arduino
  Try again

## Slide 16: 2. Write Code, or….

## Slide 17: 3. Load Example

## Slide 18: 3a. Blink Example

## Slide 19: 4. Upload to Arduino

## Slide 20: Lab activity 1 - Familiarisation
Obtain an Arduino dev. kit from the helpdesk
  you will need your student card to sign it out
Upload the blink example
  This flashes the on-board LED
Connect a single LED to pin 13 and GND
Using the PhysicalPixel example, modify your code so that you can turn the LED on and off from the computer keyboard.

## Slide 21
Putting it all
Together…